## Slide 1
AI-DRIVEN ARCHITECTURAL DESIGN
▲ TerraPilot
An AI co-pilot that turns plain prompts into site-aware, optimized, explainable architecture.
AI Logic & Optimization
Shape & Manipulation
Site & Urban Context
Overview
"You describe a building in a simple prompt — TerraPilot generates, places, and optimizes it on a real site."

## Slide 2
THE IDEA
From a sentence to a site-aware building
Early-stage design is slow and manual — one massing study can take days. TerraPilot collapses that into minutes through a guided, conversational workflow.
💬 You talk to it
No menus to learn. Just say it — “give it a futuristic twist”, “open it toward the park” — like talking to a design assistant.
🌍 On a real site
It knows the actual roads, sun, wind and neighbours around your plot — not a blank canvas.
🧠 And it explains
Every change carries an intent, a confidence, and a WHY. It tells you what's real vs estimated.
2000 m
OSM context radius
16
scoring objectives
8
named strategies
3
understanding layers

## Slide 3
THE JOURNEY
One guided workflow, seven stages
📍
01 Site
Define the plot.
⬡
02 Boundary
Auto setbacks.
🛰
03 Context
OSM digital twin.
◈
04 Shape
Generate & edit.
⚙
05 Optimize
Multi-objective Pareto.
▦
06 Compare
Side by side.
⬇
07 Export
Rhino / Revit IFC.
Backend enforces the order: shape generation + selection must precede optimization.

## Slide 4
SYSTEM DESIGN
How the frontend & backend work together
🖥 Frontend · vanilla JS
copilotClient.js
Routes your message to the right action
core/store.js
Single source of truth — UI reacts to state
views/viewerView.js
3D building — extrudes each floor plate at its Z
panels/healthDashboard.js
Live scores, re-evaluates on every edit
⚙ Backend · FastAPI
connection/routes/
API endpoints — thin wrappers, no duplicated logic
connection/nodes/
3-layer prompt understanding
notebook_logic/
Geometry engine — manipulate, transform, floor plates
optimization/
16 scorers + Pareto selector + env data
One shared runtime — the notebooks and the UI call the same engine. JSON over HTTP between them.

## Slide 5
END TO END
Watch a prompt flow through the system
“Give it a futuristic twist” — from the chat box to the sculpted 3D building.
💬
Chat input
User types intent
copilotClient.js
→
🔀
API route
/feedback endpoint
feedback_routes.py
→
🧠
Understand
3-layer → intent + WHY
nodes/
→
📐
Geometry op
twist the plate stack
notebook_logic
→
🧊
3D viewer
building updates live
viewerView.js
① Intent: change_character ② Op: twist · confidence 0.9 ③ Plates re-transformed, holes kept ④ Response → store → viewer re-renders
Every hop is real — the same path runs for a command, a vague intent, or "align to the road".

## Slide 6
STAGE 1–3
A digital twin of the surroundings
▸ Real OpenStreetMap data in a 2 km radius
Roads, transit, parks, amenities & neighbouring buildings
▸ Edge intelligence — every site edge named by compass
"north edge", "road-facing edge" become design targets
▸ 10 context scores computed once & cached
Feeds noise, view, access & density objectives later
▸ Automatic setbacks define the buildable area
Nothing can be placed outside it
● Live Design Health
☀ Solar █████████ 66
👁 View ██████████████ 98
🔊 Noise ██ 14
💨 Wind █████████ 64
🏢 Density ████████ 56
Draggable · minimizable · updates live · shows geometry → real data

## Slide 7
STAGE 4 · MANIPULATION
Sculpt the building by talking to it
💬 “Design me an 8-storey tower”
→ “give it a futuristic twist”
→ “carve a courtyard”
→ “add 2 floors on the right wing”
Real geometry updates live in 3D after every prompt.
▸ Natural-language intent, not commands
“Give it a futuristic twist”, “carve a courtyard”
▸ Floor-plate model — a stack of plates
Edit per-floor AND per-wing, not the whole block
▸ Real geometry every time
Holes, wings & twist travel through every transform
▸ Save any version
→ preview & optimize it later

## Slide 8
THE BRAIN
How we break & understand a prompt
Every message flows through a 3-layer pipeline — most specific first, smartest fallback last.
⌨️ LAYER 1
Direct command
Exact instructions — “add 2 floors”, “rotate 30°”.
→
🧩 LAYER 2
Semantic intent
The LLM reads a feeling — “let in more daylight”.
→
🧠 LAYER 3
Reason Node
Decides the move + the WHY, with confidence.
🔁 Two-tier fallback
Gemini → Cloudflare → keyword matching. It never dies on an API quota — the fallback is load-bearing.
🛡️ Hallucination guard
If a prompt matches no real operation, we reject it — never fake a change to look successful.

## Slide 9
THE ENGINE
Multi-objective optimization
🎲 POOL — Candidates
Placement × rotation × massing — large, diverse pool.
📊 SCORE — Every objective
16 scorers per candidate, cached site memory.
⭐ SELECT — 8 strategies
Diverse, named options from the Pareto front.
True Pareto front
A diverse set of non-dominated options — each best at a different trade-off, so you choose by priority, not a single 'winner'.
☀ Solar 👁 View 🔊 Noise
🌳 Open 💨 Wind ⚖ Balanced
Honest engineering: scores use real NASA POWER climate + OSM data. Missing data shows N/A, never invented.

## Slide 10
DEPTH
The hard problems we solved
🌀 Optimize keeps your edits
Optimizing a manipulated building preserves the twist + added floors — the full floor-plate stack is carried through every step.
🗂️ Saved-shapes explorer
Browse saved designs → preview each in 3D → optimize the exact one you choose. Variants accumulate, never overwrite.
🛣️ Context-aware alignment
"Align facade to main road" rotates the building parallel to the real OSM road geometry — not a compass default.
All 6 environmental scorers run in dual mode — a geometry estimate AND a real-data value — with a proxy / ● live badge, so you always know which is which.

## Slide 11
UNDER THE HOOD
The backend, in one picture
FastAPI runtime
▸ One shared engine — notebooks & UI
Routes are thin wrappers over notebook_logic
▸ nodes/ — 3-layer prompt understanding
direct → semantic → reason-node
▸ optimization/ — 16 scorers + Pareto
env_data · site_context_memory · context_enrichment
Data & intelligence
▸ NASA POWER — wind, solar, temperature
Fetched once per site, cached
▸ OpenStreetMap — roads, amenities, buildings
Powers noise, access, density, road-align
▸ Shape version manager
Save / preview / optimize — floor-plate geometry preserved

## Slide 12
UNDER THE HOOD
The agent's state graph — every prompt's path
A supervisor (central_reason) picks the next action; each node writes its result to shared state and returns to the planner. Drawn straight from agent/graph.py.
START → planner
builds the plan
central_reason
supervisor — picks next action
read_site
↑ writes to state → planner
generate_shape
↑ writes to state → planner
check_constraints
↑ writes to state → planner
optimize
↑ writes to state → planner
evaluate
↑ writes to state → planner
place_building
↑ writes to state → planner
report → finish
↑ writes to state → planner
await_human → finish
↑ writes to state → planner
Nodes don't hand off to each other — each writes its result to shared state, then returns to the planner, which reads it and plans the next step.

## Slide 13
HONEST STATUS
What works — and what doesn't yet
✅ What works today
• Plain-prompt generation, manipulation & per-wing floor edits
• Multi-objective optimization with a true Pareto front
• Real environmental scoring — NASA + OpenStreetMap
• Context-aware moves — "align to the road", "face the park"
• Save / preview / optimize saved versions end-to-end
🚧 Current limitations
• A scoring engine, not a full physics simulation
• LLM intent depends on a free-tier quota (keyword fallback covers it)
• Export is GeoJSON today; native Rhino/Revit needs the MCP bridge
• Single building per site; massing is conceptual
• Context quality depends on OpenStreetMap coverage
We're deliberate about honesty: when data or a model isn't available, TerraPilot says so — never invents a number.

## Slide 14
WHY DESIGNERS CARE
How it helps a designer
⚡ Explore in minutes, not days
Test dozens of site-aware options in the time a single massing study used to take.
🌍 Site-grounded from the first sketch
Sun, wind, noise, roads and neighbours are in the loop from minute one.
🗣️ No software to learn
Designers think in intent, not menus. “Open it toward the park” just works.
🧾 Decisions you can defend
Every move carries a WHY and a score trade-off — a clear story for clients & juries.
TerraPilot doesn't replace the designer — it removes the grunt work so they spend time on judgement, not setup.

## Slide 15
Plain prompts in.
Site-aware architecture out.
▲ TerraPilot · An AI co-pilot for early-stage architectural design